## Slide 1: GPS L2C SDR

## Slide 2
Signals |  | Code Freq. | Code Len. | Nav. Data |  | Modulation | Freq. | Band Width | Min. Received Power[dBW]
 |  | [Mcps] | [chip] | Type | D(t)/d(t)[bps] |  | [MHz] | [MHz] | 
L1 C/A |  | 1.023 | 1023 | NAV | 50/50 | BPSK-R(1) | 1572.42 | 2.046 | -158.5
L1 P(Y) |  | 10.23 | 7 days | NAV | 50/50 | BPSK-R(10) |  | 20.46 | -161.5
L1 M |  | 5.115 | Unknown | MNAV | Unknown | BOC(10,5) |  | 30.69 | Unknown
L1C | L1 CD | 1.023 | 10230 | CNAV-2 | 50/100 | BOC(1,1) |  | 4.092 | -157.0
 | L1 CP | 1.023 | 10230×1800 | Pilot Channel |  | TMBOC(6,1,4/33) |  | 14.332 | 
L2 P(Y) |  | 10.23 | 7 days | NAV | 50/50 | BPSK-R(1) | 1227.6 | 20.46 | -161.5
L2C | CM | 0.5115×2 | 10230 | CNAV | 25/50 | BPSK-R(1) |  | 2.046 | -160.0
 | CL |  | 767250 | Pilot Channel |  |  |  |  | 
L2M |  | 5.115 | Unknown | MNAV | Unknown | BOC(10,5) |  | 30.69 | Unknown
L5C | L5I | 10.23 | 10230×10 | CNAV | 50/100 | QPSK-R(10) | 1176.45 | 20.46 | -157.9
 | L5Q | 10.23 | 10230×20 | Pilot Channel |  |  |  | 20.46 | 
Introduction (1/8)
  GPS signal parameters

## Slide 3
Introduction (2/8)
List of SVs transmitting L2C (*)
Satellite | Launch (UTC) | Launch site | Block | № | SVN | PRN | Slot
USA-266 | 2/5/2016 | CCAFS SLC-41 | IIF | 12 | 70 | 32 | F5
USA-265 | 10/31/2015 | CCAFS SLC-41 | IIF | 11 | 73 | 10 | E6
USA-183 | 9/26/2005 | CCAFS SLC-17A | IIRM | 1 | 53 | 17 | C4
USA-190 | 9/25/2006 | CCAFS SLC-17A | IIRM | 2 | 52 | 31 | A2
USA-192 | 11/17/2006 | CCAFS SLC-17A | IIRM | 3 | 58 | 12 | B4
USA-196 | 10/17/2007 | CCAFS SLC-17A | IIRM | 4 | 55 | 15 | F2
USA-199 | 12/20/2007 | CCAFS SLC-17A | IIRM | 5 | 57 | 29 | C1
USA-201 | 3/15/2008 | CCAFS SLC-17A | IIRM | 6 | 48 | 7 | A4
USA-206 | 8/17/2009 | CCAFS SLC-17A | IIRM | 8 | 50 | 5 | E3
USA-213 | 5/28/2010 | CCAFS SLC-37B | IIF | 1 | 62 | 25 | B2
USA-232 | 7/16/2011 | CCAFS SLC-37B | IIF | 2 | 63 | 1 | D2
USA-239 | 10/4/2012 | CCAFS SLC-37B | IIF | 3 | 65 | 24 | A1
USA-242 | 5/15/2013 | CCAFS SLC-41 | IIF | 4 | 66 | 27 | C2
USA-248 | 2/21/2014 | CCAFS SLC-37B | IIF | 5 | 64 | 30 | A3
USA-251 | 5/17/2014 | CCAFS SLC-37B | IIF | 6 | 67 | 6 | D4
USA-256 | 8/2/2014 | CCAFS SLC-41 | IIF | 7 | 68 | 9 | F3
USA-258 | 10/29/2014 | CCAFS SLC-41 | IIF | 8 | 69 | 3 | E1
USA-260 | 3/25/2015 | CCAFS SLC-37B | IIF | 9 | 71 | 26 | B5
USA-262 | 7/15/2015 | CCAFS SLC-41 | IIF | 10 | 72 | 8 | C5
(*) Wikipedia: https://en.wikipedia.org/wiki/List_of_GPS_satellites
19 Svs

## Slide 4
Introduction (3/8)
Modulation scheme for the GPS L2 Signals
  Time multiplexed
  Chipping rate is doubled
  Synchronized with the X1 epochs of the P-code.
CM/CL Codes:

## Slide 5
Introduction (4/8)
Spectra of the GPS Signals in L2 (*)
(*) Wikipedia: http://www.navipedia.net/index.php/GPS_Signal_Plan

## Slide 6
Introduction (5/8)
Fig. 3-12 of IS-GPS-200H
L2 CM/CL code timing relationship

## Slide 7
Introduction (6/8)
CNAV message
Fig. 3-14 of IS-GPS-200H
  ½ ficxed convolutional code + CRC-24Q
  Viterbi Decoder / Fano Decoder
  Same as Galileo I/NAV

## Slide 8
Introduction (7/8)
Message structure of CNAV
  Forward error correction (FEC) encoded by 1/2 convolutional code.
  Transmit a complete ephemeris every 48 seconds.

## Slide 9
Introduction (8/8)
CNAV Message contents
Type No. | Message Content | Max. Broadcast Intervals
10 | Ephemeris | 48 seconds
11 | Ephemeris | 48 seconds
30-37 | Clock | 48 seconds
30 | Inter-Signal Correction and Ionospheric Data | 288 seconds
33 | UTC | 288 seconds
35 | GPS/GNSS Time Offset | 288 seconds
31 or 12 | Reduced Almanac | 20 minutes
34 or 13 | Differential Correction | 30 minutes
32 | Earth Orientation Parameters | 30 minutes
14 | Differential Correction | 30 minutes
37 | Midi Almanac | 2 hours
36 or 15 | Text Message | Not determined
Requisite for receiver fix:
Type 10
  Type 11
  Any one of 30-37

## Slide 10
SDR processing procedure

## Slide 11
initSettings.m (1/2)
Acquisition settings
- Single sideband for carrier freq. search
  settings.acqSearchBand = 5000;
- Coherent integration time for acquisition can be set to 0 -20 (ms) by users
  settings.acqCohT = 20;
- Carrier freq. search step
  settings.acqStep = 1000/settings.acqCohT/2;
  - Sampling rate threshold for downsampling
      If input signal sampling freq. is too high for FFT computation, it can be resampled to a lower freq. to save processing time.
  settings.resamplingThreshold = 8e6;
  - Enable/dissable use of downsampling for acquisition
  settings.resamplingflag = 1; % 0 – Off, 1 - On

## Slide 12
initSettings.m (2/2)
  Tracking loops settings
  - PLL and DLL integration time equals the CM code length
  settings.intTime = 0.02;
  Code parameter setting
  - L2 CM code rate is 0.5115 Mcps, and the code length is 10230 chips.
  settings.codeLength = 10230;
  settings.codeFreqBasis = 0.5115e6;
  Velocity computation setting
  - L2 carrier frequency
  settings.carrFreqBasis = 1227.60e6;
  - Half number of carrier frequencies used to do Doppler smoothing
  settings.dopSmoothNr = 2;

## Slide 13
acquisition.m (1/14)
  Acquisition Method
  - Circular correlation by Zero-padding FFT
  - Perfect correlation can be obtained even when navigation bit is changed.
  - Computation is doubled.

## Slide 14
acquisition.m (2/14)
  Acquisition Method
  - Circular correlation by Zero-padding FFT

## Slide 15
acquisition.m (3/14)
  Acquisition Method
  - Circular correlation by Zero-padding FFT
  Case 3

## Slide 16
acquisition.m (4/14)
  Selectable downsampling
  - Computational load
  setsettings.acqCohT = 20;
  setsettings.samplingFreq = 53e6;
  - Computers crash all the time with MATLAB.
  - How to settle this problem?
2120000-point FFT
  Downsampling
  How?

## Slide 17
acquisition.m (5/14)
  Bandpass sampling theory
  - Assume that a real single-sideband is located at , where and are given by , , is the information bandwidth, and is the center of frequency of the information band. To avoid harmful signal spectral folding in reconstructing the signal, acceptable sampling rate should be in the range of
  denoting the largest integer less than or equal to .

## Slide 18
acquisition.m (6/14)
  Acquisition implementation
  - Selectable downsampling
  (1) Filter out signal power outside the main lobe of CM code to avoid spectral folding
  fs = settings.samplingFreq;
  IF = settings.IF;
  BW = 1.2e6*2;
  w1 = (IF)-BW/2;
  w2 = (IF)+BW/2;
  wp = [w1*2/fs-0.002 w2*2/fs+0.002];
  b = fir1(700,wp);
  longSignal = filtfilt(b,1,longSignal);
Power spectral density after digital bandpass filtering

## Slide 19
acquisition.m (7/14)
  Acquisition implementation
  - Selectable downsampling
  (2) Calculate upper and lower boundary of the acceptable sampling Freq. range:
  fu = settings.IF + BW/2;
  n = floor(fu/BW);
  if (n<1)
  n = 1;
  end
  lowerFreq = 2*fu/n;
  fl = settings.IF - BW/2;
  if(n>1)
  upperFreq = 2*fl/(n-1);
  else
  upperFreq = lowerFreq;
  end

## Slide 20
acquisition.m (8/14)
  Acquisition implementation
  - Selectable downsampling
  (3) Find downsampling frequency
  Take the center of the acceptable sampling Freq. range as downsampling frequency.
  settings.samplingFreq = ceil((lowerFreq + upperFreq)/2);
  (4) Downsample input IF signals
  signalLen = floor((length(longSignal)-1) /oldFreq * settings.samplingFreq);
  index = ceil((0:signalLen-1)/settings.samplingFreq * oldFreq);
  index(1) = 1;
  longSignal = longSignal(index);

## Slide 21
acquisition.m (9/14)
  Acquisition implementation
  - Selectable downsampling
  (5) Equivalent IF after downsampling
  Resampling is equivalent to down-converting the original IF by integer times of resampling freq.
  settings.IF = rem(settings.IF,settings.samplingFreq);
Power spectral density after downsampling

## Slide 22
acquisition.m (10/14)
  Acquisition implementation
  - Coarse acquisition
  Finding the second largest peak is a little different from the L1 C/A SDR.
  …
  codePhaseRange = [leftRange rightRange];
  …

## Slide 23
acquisition.m (11/14)
  Acquisition implementation
  - Fine acquisition
  Signal length (findLen) used to do fine acquisition depends on settings.acqCohT.
  if(settings.acqCohT <=10)
  findLen = samples10msLength;
  else
  findLen = samplesXmsLen;
  end
  - Change fine acquisition results to correspond with original sampling frequency, if downsampling is carried out.
  acqResults.codePhase(PRN) = floor((codePhase - 1)/ ...
  settings.samplingFreq *oldFreq)+1;
  doppler = acqResults.carrFreq(PRN) - settings.IF;
  acqResults.carrFreq(PRN) = doppler + oldIF;

## Slide 24
acquisition.m (12/14)
 | With Downsampling* | Without Downsampling**
Elapsed time | 255.8 second | 2624.3 second
Processing time of acquisition
(*) settings.acqCohT = 10; settings.resamplingflag = 1; settings.acqSatelliteList = 1:32;
(**) settings.acqCohT = 10; settings.resamplingflag = 0; settings.acqSatelliteList = 1:32;
  Acquisition Results

## Slide 25
acquisition.m (13/14)
  Acquisition Results
With Downsampling*
Without Downsampling**
(*) settings.acqCohT = 10; settings.resamplingflag = 1; settings.acqSatelliteList = 1:32;
(**) settings.acqCohT = 10; settings.resamplingflag = 0; settings.acqSatelliteList = 1:32;

## Slide 26
acquisition.m (14/14)
  Acquisition Results
PRN | With Downsampling* |  | Without Downsampling** | 
 | Doppler | Code offset | Doppler | Code offset
12 | -1459 | 193394 | -1463 | 193391
6 | 1033 | 356347 | 1039 | 356345
5 | -3497 | 701963 | -3504 | 701962
25 | -3030 | 621140 | -3030 | 621139
17 | 1181 | 879013 | 1190 | 879015
24 | 1534 | 829119 | 1525 | 829115
29 | -2928 | 933179 | -2935 | 933174
(*) settings.acqCohT = 10; settings.resamplingflag = 1; settings.acqSatelliteList = 1:32;
(**) settings.acqCohT = 10; settings.resamplingflag = 0; settings.acqSatelliteList = 1:32;

## Slide 27
tracking.m (1/4)
  A 3-order PLL was used to improve dynamic performance of carrier tracking

## Slide 28
tracking.m (2/4)
  PLL filter coefficients calculation
  [pf3,pf2,pf1] = calcLoopCoefCarr(settings);
  NCO update
  d2CarrError = d2CarrError + carrError * pf3;
  dCarrError = d2CarrError + carrError * pf2 + dCarrError;
  carrNco = dCarrError + carrError * pf1;
  Save remCodePhase for pseudorange calculation
  trackResults(channelNr).remCodePhase(loopCnt) = remCodePhase;

## Slide 29
tracking.m (3/4)
  Tracking results
  - With complex IF data set
  (L2_USRPL1L2_1950secIn_fs_4e6_if20e3_schar.bin) – referred to as Data Set 1
  Both PLL and DLL work well.
PRN # 29

## Slide 30
tracking.m (4/4)
  Tracking results
  - With scalar IF data set (L2c_60s.bin) – referred to as Data Set 2
  DLL works well and position accuracy is acceptable.
  PLL tracking of all channels not stable.
PRN # 12
Why?

## Slide 31
  The maximal polynomial is 1112225171 (octal) of degree 27.
  Initialized at the P-coder X1 epoch.
  PRN is assigned to PRN #1-63 and #159-210.
  Short cycled every count period of 10,230
generateCMcode.m (1/3)
Characteristics of CM code

## Slide 32
generateCMcode.m (2/3)
  Generating procedure
  - (1) Set generating polynomial
  RegPos = [4 7 9 12 15 17 19 22 23 24 25];
  - (2) Initial-state table (See “IS-GPS-200H” for more details)
  l2cm_init = [...];
  - (3) Select initial states for PRN
  if (PRN >= 1 && PRN <= 63)
  shiftPos = PRN;
  elseif(PRN >= 159 && PRN <= 210)
  shiftPos = PRN - 95;
  elseif ( PRN < 1 || PRN > 210 || (PRN >= 64 && PRN <= 158) )
  disp(' PRN does not exist! ');
  return;
  End
  code_init = l2cm_init(shiftPos);

## Slide 33
generateCMcode.m (3/3)
  Generating procedure
  - (4) Covert octal format to binary bit and fill in shift register
  reg = dec2bin(oct2dec(code_init)) - 48;
  reg = [zeros(1,27-length(reg)) reg];
  - (5) Generate CM code
  CMcode = zeros(1,CodeLength);
  for index = 1:CodeLength
  CMcode(index) = reg(end);
  reg = circshift(reg',1)';
  reg(RegPos) = reg(RegPos) * CMcode(index);
  end

## Slide 34
makeCMTable.m (1/1)
  Return zero (RZ) CM code are generated
  cmCode = generateCMcode(PRN,settings);
  cmCode = [cmCode;zeros(1,length(cmCode))];
  cmCode = reshape(cmCode,1,[]);

## Slide 35
postNavigation.m (1/3)
  Main changes
  - CNAV data and ephemeris decoding
  See “CNAVdecoding.m” and “ephemeris_L2CM.m”
  - Calculation of signal transmitting time
  See “calculatePR_PRR.m”
  - Calculation of pseudorange and rate
  See “calculatePR_PRR.m”
  - Position and Velocity computation for SVs
  See “satposvel_L2C.m”
  - Add velocity computation
  See “leastSquarePosVel.m”

## Slide 36
postNavigation.m (2/3)
  Main changes
  - Start and end of measurement points
  Measurement point begins at the latest start of first messages of all channels (firstSubFrame), and consider Doppler smoothing
  for channelNr = activeChnList
  sampleStart(channelNr) = ...
  trackResults(channelNr).absoluteSample(firstSubFrame(channelNr));
  sampleEnd(channelNr) = trackResults(channelNr).absoluteSample(end);
  End
  …
  - Correct pseudorange rate for SV clock rate error
  clkCorrRawPRat = rawPRat(activeChnList) + satClkCorrRat * settings.c;
  localTime = localTime + measSampleStep/settings.samplingFreq ;

## Slide 37
postNavigation.m (3/3)
  Main changes
  - Correct and save local time
  localTime = localTime - xyzdt(4)/settings.c;
  navSolutions.localTime(currMeasNr) = localTime;
  - Convert velocity in ECEF to ENU
  Use function “ECEF2ENU.m”
  - Save velocity results
  navSolutions.Ve(currMeasNr) = ENU(1);
  …
  - Update local time
  Except first time, local time is updated by measurement step
  localTime = localTime + measSampleStep/settings.samplingFreq ;

## Slide 38
CNAVdecoding.m (1/4)
  Viterbi decoder algorithm
  MATALB function: decoded = vitdec(code,trellis,tblen,opmode,dectype)

## Slide 39
CNAVdecoding.m (2/4)
  Implementation procedure

## Slide 40
CNAVdecoding.m (3/4)
  Implementation details
  - Prepare trellis description for Viterbi decoder
  trellis = poly2trellis(7,[171 133]);
  - Search the first G1 output bit and do Viterbi decoding
  for bitSync = 1:2
  decodedBits = vitdec(I_P_InputBits(bitSync:end-(bitSync-1)),
  trellis,tblen,'trunc','hard');
  …
  end
  - Find all possible preambles
  index = find(round(abs(tlmXcorrResult(xcorrLength : xcorrLength * 2 - 1))) == 8.00)';
  - Correct polarity of the CNAV data bits
  if(~isequal(navBits(1:8),preamble_01))
  navBits = not(navBits);
  End

## Slide 41
CNAVdecoding.m (4/4)
  Implementation details
  - CRC-24Q check
  See MATLAB Communications System Toolbox for details
  crcDet = comm.CRCDetector([24 23 18 17 14 11 10 7 6 5 4 3 1 0]);
  [~,frmError] = step(crcDet,navBits(1:300)')
  - Ephemeris decoding and TOW
  See “ephemeris_L2CM.m”
  - “firstSubFrame”
  Start position of the first message in I_P stream
  firstSubFrame = index(i) * 2 + bitSync - 2;

## Slide 42
ephemeris_L2CM.m (1/1)
  Ephemeris decoding
  - No special technique is needed.
  - For more details, refer to “IS-GPS-200H”.
  Compute TOW of the first message
  - Every message lasts 12 second.
  TOW = bin2dec(navBitsBin(21:37)) * 6 - 12;

## Slide 43
calculatePR_PRR.m (1/2)

## Slide 44
calculatePR_PRR.m (2/2)
  pseudoranges = (localTime - transmitTime) * settings.c;
  pseudorangesRat = - doppler * (settings.c /settings.carrFreqBasis);

## Slide 45
satposvel_L2C.m (1/3)
  SV position calculation differences from L1 C/A SDR
  - Semi-Major Axis at reference time
  A_0 = A_REF + eph(prn).deltaA;
  A = A_0 + eph(prn).ADot * tk;
  - Mean motion difference from computed value
  delta_n = eph(prn).delta_n_0 + 0.5 * eph(prn).delta_n_0Dot *tk;
  - Rate of right ascension
  omegaDot = omegaDot_REF + eph(prn).delta_omegaDot;
  Inter-Signal Correction depends on decoding of message type # 30 (IS-GPS-200H, P171)
  if(eph(prn).idValid(3) == 30)
  satClkCorr(satNr) = satClkCorr(satNr) - eph(prn).T_GD + eph(prn).ISC_L2C;
  end

## Slide 46
satposvel_L2C.m (2/3)
  SV velocity calculation
  - Same as using NAV ephemeris
  - No special technique is needed. For more details, refer to:
  Korvenoja P., Piche R. Efficient satellite orbit approximation. Proceeding of ION GPS, Salt Lake City, UT, Sep. 19-22, 2000.

## Slide 47
satposvel_L2C.m (2/3)
  Clock rate correction
  where, - SV clock drift correction coefficient
  - SV clock drift rate correction coefficient
  - relativistic correction term
  where,
  - Semi-Major Axis
  - eccentric anomaly
  dtrRat = F * eph(prn).e * sqrt(A) * cos(E) *dE;
  satClkCorrRat(satNr) = 2* eph(prn).a_f2 * dt + eph(prn).a_f1 + dtrRat;

## Slide 48
leastSquarePosVel.m (1/2)
  Receiver position calculation
  - Not changed
  Receiver velocity calculation
  =
  where, - pseudorange rate corresposnding to SV
  - velocity of SV
  - unit vector form receiver to SV
  - same as position computation

## Slide 49
leastSquarePosVel.m (2/2)
  Receiver velocity calculation
  for i = 1:nmbOfSatellites
  rvetor = (satpos(:, i) - pos(1:3)')/ norm(satpos(:, i) - pos(1:3)', 'fro');
  omcPRat(i) = ObsPRat(i) - dot(satvel(:, i), rvetor);
  end
  vel = A \ omcPRat;

## Slide 50
Fix results (1/2)
With Data Set 2

## Slide 51
Fix results (1/2)
With Data Set 2

## Slide 52
Still unresolved problems (1/2)
  Receiver velocity calculation
  - With Data Set 1
  Doppler values of all channels are opposite to the true values.
  By adding the following lines in “leastSquarePosL2CM.m”, right velocities can be obtained
  if (settings.fileType == 2)
  omcPRat(i) = ObsPRat(i) + dot(satvel(:, i), rvetor);
  else
  omcPRat(i) = ObsPRat(i) - dot(satvel(:, i), rvetor);
  end

## Slide 53
Still unresolved problems (2/2)
  Receiver velocity calculation
  - With Data Set 2
  Doppler and velocity values of all channels are
  completely wrong.

## Slide 54
References
  IS-GPS-200H, Navstar GPS Space Segment/Navigation User Interfaces. Sep. 24, 2013.
  Korvenoja P., Piche R. Efficient Satellite Orbit Approximation. Proceeding of ION GPS, Salt Lake City, UT, Sep. 19-22, 2000.
  Yi-Ran Sun. Generalized Bandpass Sampling Receivers for Software Defined Radio. Doctoral thesis. 2006.
  Hang Yin. An Adaptive Multi-frequency GPS Tracking Algorithm, GPS CNAV Message Decoding, and Performance Analysis. Master thesis. 2014.

## Slide 55
Future Works
Refine the SDR
- Advanced algorithm
- Processing speed
- Clear Comment
Add L2 CL code acquisition, tracking and PVT computation
- Improve sensitivity

## Slide 56: Thank you! Yafeng Li @ Beijing institute of technology lyf8118@126.com